## Slide 1
Pre-processing and multi-temporal analysis of SAR time series
Magdalena Fitrzyk

## Slide 2
Part 1
Multitemporal Analysis of SAR Backscatter Intensity

## Slide 3: Objectives
Familiarizing with SNAP toolbox
Familiarizing with Sentinel-1 GRD prodcucts
Calculation of backscatter intensity from Sentinel-1 detcted products
Analysis of temporal backscatter signatures for various land cover types
Change detection over AOI (Beijing Daxing International Airport)

## Slide 4: Introduction
S1A_IW_GRDH_1SDV_20151003T222044_20151003T222111_007994_00B2F6_9374 S1A_IW_GRDH_1SDV_20160611T222046_20160611T222112_011669_011DDC_7FB0 S1B_IW_GRDH_1SDV_20171115T222014_20171115T222041_008298_00EAE8_2415 S1B_IW_GRDH_1SDV_20181110T222021_20181110T222048_013548_019131_A556 S1B_IW_GRDH_1SDV_20190930T222028_20190930T222054_018273_022698_C498
Input data: time series of Sentinel-1 GRDH images over China
Output:
temporal backscatter signatures for various land cover types
change detection

## Slide 5: Data preparation
1. Opening the S1 data
For unzipped products

## Slide 6: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 7: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 8: Updating orbits
Radar / Apply orbit file
POEORB - few weeks after acq.
The orbit file provides accurate satellite position and velocity information. Based on this information, the orbit state vectors in the abstract metadata of the product are updated.
RESORB – within few hours

## Slide 9: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 10: Radiometric Calibration
Beta Naught – radar brightness coefficient, reflectivity per unit area in slant range which is dimensionless
Sigma Naught – power returned to the antenna from the ground (distributed scatterer) in dB. A number comparing the strangth of the signal to that expected from and area of one square meter. It is defined with respect to the nominal horisontal plane and is varying with incidence angle, wavelength, polarisation and scattering surface itself
From image pixel values or digital numbers (DNs) we can derive:

## Slide 11: Radiometric Calibration
Pixel values can be directly related to the radar backscatter
Radar/Radiometric/Calibrate

## Slide 12: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 13: Terrain correction & Geocoding
Point B with elevation h above the ellipsoid is imaged at position B’ in SAR image, though its real position is B". The offset between B' and B" exhibits the effect of topographic distortions
Terrain Correction allows geometric overlays of data from different sensors and/or geometries.

## Slide 14: Terrain correction & Geocoding
Radar / Geometric / Terrain Correction / Range Doppler Terrain Correction

## Slide 15: Terrain correction & Geocoding
DEM selection
Pixel spacing
Map projection
Masking areas without elevation

## Slide 16: Data check

## Slide 17: Automatic Processing with Graph
Graph Builder
Inserting blocks with particular processing operators
(right mouse button)
Save the graph and/or Run

## Slide 18: Automatic Processing with Graph – Calibration, Terrain Correction
save as GRD_Cal_TC.xml
The same settings like in manual processing
Apply Orbits: Sentinel Precise
Calibration: Output Sigma0
Terrain Correction: pixel spacing 10m

## Slide 19: Batch processing
Adding data products
Batch processing tool
Loading the graph

## Slide 20: Batch processing
Open previously saved graph GRD_Cal_TC.xml

## Slide 21: Time series analysis
Add your data products

## Slide 22: Time series analysis
Bands filter
Show plot at cursor position
Choose your processed data products

## Slide 23: Time series analysis
One of the plottet bands has to be opened

## Slide 24: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 25: Creating multitemporal stack
Product geolocation (if terrain corrected)
Orbits (if not terrain corrected)
Collocating spatially overlapping images

## Slide 26: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 27: Multitemporal speckle filtering
Spatial filtering with weighted average of selected filter across the images of the time series

## Slide 28: Multitemporal speckle filtering
Not filtered
Filtered

## Slide 29: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 30: Conversion from linear to dB

## Slide 31: Conversion from linear to dB

## Slide 32: Linear vs dB comparison

## Slide 33: Data processing
Creating a subset of S1 GRDH images
Spatial subset depending on the AOI
Updating orbits
Radiometric calibration
  Conversion of image intensity to sigma0 providing the radar backscatter
Terrain correction
Compensate for geometric distortions caused by topographical variations of a scene and the tilt of satellite sensor
Creating a multitemporal stack
  Collocation spatially overlapping products (based on geolocation)
Speckle filtering
    Filtering the inherent salt and pepper like texturing called speckles
Linear to dB conversion
    Compensate for very high dynamic range in visualisation
Stack statistics and analysis of temporal backscatter signatures

## Slide 34: Visual inspection of the time series

## Slide 35: RGB Composite
Right click on the product
Band selection

## Slide 36: RGB Composite
Red – high backscatter in 2015, low backscatter in 2019
Cyan – low backscatter in 2015, high in 2019

## Slide 37: Stack averaging

## Slide 38: Stack averaging – RGB Composite
RGB combination for land cover classification

## Slide 39: Image statistics
Choose your band

## Slide 40: Image statistics - polygon
Draw the polygon