## Slide 1
Fabrizio Ramoino
ESA/ESRIN
Practical on pre-processing of optical time series including S2

## Slide 2: Practical on pre-processing of optical time series including S2
Overview of Sentinel-2
  Spectral bands
  Level 2A products
Pre-processing chain starting from S2 L2A data
  Resampling
  Subset
  Band Maths
  Radiometric Indices
  S2 Biophysical processor
Graph Builder
Batch Processing
Time series analysis

## Slide 3: Sentinel-2 spectral bands

## Slide 4: Sentinel-2 L2A data overview
Sen2Cor is the Atmospheric Correction processor used in the ESA Payload Data Ground Segment to generate S2 L2A data and it is distributed via STEP to be used as SNAP plug-in or via command line.
Bottom-of-atmosphere (BOA) reflectances in cartographic geometry (UTM/WGS84)
Products additionally include:
  Scene Classification Map
  Water Vapor Map
  Aerosols Optical Thickness Map
Algorithm includes:
  Cloud and cloud shadow detection
  Cirrus detection and correction
  Slope effect correction
  BRDF effect correction
Beyond Sen2Cor, Sentinel-2 data can be atmospherically corrected using others processors:
MAJA (developed by CESBIO/CNES)
i-COR (developed by VITO)
CorA (developed by Brockmann Consult)
LaSRC (developed by NASA GSFC/USA)
……

## Slide 5: Sentinel-2 L2A data overview
From left to right:
Level-1C [TOA]
[RGB] B4-B3-B2
[RGB] B12-B11-B8a
Level-2A [BOA]
Scene Classification
[RGB] B4-B3-B2
[RGB] B12-B11-B8a
Water Vapour
Aerosols Optical Thickness

## Slide 6: Sentinel-2 pre-processing
Essential pre-processing steps:
Resampling
The S2 products are multi-size
B2, B3, B4 and B8 @ 10m
B5, B6, B7, B8A, B11 and B12 @ 20m
B1, B9 and B10 @ 60m
Needed if the user wants to combine bands with different spatial resolution
Subset (spatially/spectrally)
The S2 data are distributed in tiles 100x100 km2 ortho-images in UTM/WGS84 projection.
Needed if the AOI covers a portion of the S2 scene or if only a subset of bands are useful in the next step (this will reduce the computation time)
Re-projection
If the AOI covers more than one S2 tile in different UTM zones the user needs to re-project in a common CRS before to mosaic them.
If the user wants to merge different data sources projected in different CRS.
To export the view in KMZ and visualise your output in Google Earth.

## Slide 7: Open a Sentinel-2 data
Click on ‘File’  ‘Open Product…’  select the ‘MTD_MSIL2A.xml’ file

## Slide 8: Visualize Sentinel-2 data
S2 L1C (Refl TOA)
S2 L2A (Refl BOA)

## Slide 9: Resampling
Select the product in the Product Explorer window.
Click on ‘Raster’  ‘Geometric Operations’  ‘Resampling’
In the pop-up window set up the parameters as shown in the Figures:
Unselect ‘Save as:’
‘10m’ as pixel resolution
‘Nearest’ as Upsampling method
Click on ‘Run’

## Slide 10: Subset (spatially/spectrally)
Select the new product in the Product Explorer window.
Click on ‘Raster’  ‘Subset…’
In the pop-up window set up the parameters as shown in the Figures:
Define the X and Y pixels range or the X and Y geo-coordinates to crop the input product
Define which bands you want to export
Click on ‘Run’

## Slide 11: Band Maths (e.g. NDVI)
Select the product in the Product Explorer window.
Click on ‘Raster’  ‘Band Maths…’
In the pop-up window set up the parameters as shown in the Figures:
Change the Name: ‘NDVI’
Unselect ‘Virtual’ box
Click on ‘Edit Expression…’
Create your expression using ‘@’ and after replace them with the bands
  (@ - @) / (@ + @)
  (B8 – B4) / (B8 + B4)
Click on ‘Run’

## Slide 12: Output Visualization
When the processing is finished the output will be automatically opened in the ‘Product Explorer’ of SNAP Select the product in the Product Explorer window.
Using the Colour Manipulation (bottom left) you can modify the colour palette.

## Slide 13: Radiometric Indices
Vegetation indices
Soil indices
Water indices
SAVI, TSAVI, MSAVI, MSAVI2
DVI, RVI, PVI
NDVI, WDVI, TNDVI, GNDVI
GEMI
ARVI
NDI45
MTCI, MCARI, PSSRa
S2REP, REIP, IRECI
RI
BI
BI2
GEMI
MNDWI
NDWI
NDWI2
NDPI
NDTI
Radiometric indices are quantitative measures of features that are obtained by combining several spectral bands

## Slide 14: Radiometric Indices (e.g. NDVI)

## Slide 15: Biophysical processor (L2B)
Select the new product in the Product Explorer window.
Click on ‘Optical’  ‘Thematic Land Processing’  ‘Biophysical processor (LAI, fAPAR, …)’
In the pop-up window set up the parameters as shown in the Figures:
Unselect ‘Save as:’
Select only ‘LAI’
Click on ‘Run’
LAI: Leaf Area Index
fAPAR: Fraction of Absorbed Photosynthetically Active Radiation
FVC: Fraction of vegetation cover
Cab: Chlorophyll content in the leaf
CWC: Canopy Water Content

## Slide 16: GraphBuilder
The Graph Builder allows the user to assemble graphs from a list of available operators and connect operator nodes to their sources.
Right click on the top panel to add an Operator.

## Slide 17: GraphBuilder
We can create our processing chain adding to the default blocks ‘Read’ and ‘Write’:
‘Rempling’
‘Raster’  ‘Geometric’  ‘Resample’
‘Subset’
‘Raster’  ‘Geometric’  ‘Subset’
‘Band Maths’
‘Raster’  ‘BandMaths’
‘S2rep’ (S2 Red-Edge Position Index)
‘Optical’  ‘Them. Land Proc.’  ‘Veg. Rad. Ind.’  ‘S2repOp’
‘Biophysical Processor’
‘Optical’  ‘Thematic Land Processing’  ‘BiophysicalOp’
‘Band Merge’
‘Raster’  ‘BandMerge’

## Slide 18: GraphBuilder (Resample module)

## Slide 19: GraphBuilder (Subset module)

## Slide 20: GraphBuilder (BandMaths module)

## Slide 21: GraphBuilder (S2repOp module)
The Sentinel-2 Red-Edge Position Index algorithm is based on linear interpolation, as presented by Guyot and Baret (1988).
Red edge, as the inflection point of the strong red absorption to near infrared reflectance, includes the information of both crop (chlorophyll content) N and growth status.

## Slide 22: GraphBuilder (BiophysicalOp module)
The Biophysical Processor computes Level-2B Biophysical products from Sentinel-2 reflectances.
From Bottom Of Atmosphere normalized reflectance data, it derives a set of biophysical variables, namely:
LAI: Leaf Area Index
fAPAR: Fraction of Absorbed Photosynthetically Active Radiation
FVC: Fraction of vegetation cover
Cab: Chlorophyll content in the leaf
CWC: Canopy Water Content

## Slide 23: GraphBuilder (Band Merge module)

## Slide 24: GraphBuilder (Save the graph)

## Slide 25: Batch Processing
The Batch Processing tool allows you to execute a single reader/writer graph for a set of products. Select the Batch Processing tool from the Graphs menu and then press the "Load" button to browse for a previously saved graph. Next, add products in the I/O tab by pressing the "Add" button. Set the target folder where the output will be written to and then press "Run“.

## Slide 26: Time Series
Due to the short time you can find the batch processing output in the ‘Intermediate Output’ folder in DIMAP format.
Open them in SNAP and then open the Time Series Window. ‘View’  ‘Tool Windows’  ‘Radar’  ‘Time Series’

## Slide 27: Time Series
To populate the time series you can add all the products opened in SNAP or browsing from your disk.

## Slide 28: Time Series