## Slide 1
PolSARPro & Land Retrievals
Erxue Chen & Lei Zhao Eric Pottier
Chinese Academy of Forestry
I.E.T.R - Univ Rennes 1, FR

## Slide 2: Land cover classification from PolSAR data with PolSARPro

## Slide 3: Outlines
Introduction
GF-3 PolSAR dataset
Practical

## Slide 4: 1.1 General technique framework for remote sensing image classification
classification legend for your specific project
Class delineation & Training sample designation
Features extraction & Preliminary classification
Final classification description definition
Accuracy assessment
Class speckle filtering
Final map
Clump, sieve
Accuracy OK?
Yes
No
Ground true & reference data
Ground true & reference data
Manual editing
Training AOIs
Check AOIs
classification
I. Introduction

## Slide 5
  1.2 Classification system and legend defining
  Remote sensing classification legend
  It is the application of a classification system in a specific area using a defined mapping scale and specific data set
  Classification legend is
  Scale and cartographic representation dependent;
  Data and mapping methodology dependent.
  Classification system
  It is an abstract representation of the situation in the field using well defined diagnostic criteria
  One define it as: “The ordering or arrangement of objects into groups or sets on the basis of their relationships”
  A classification system is
  scale independent: the classes should be applicable at any scale or level of detail;
  source independent: independent of the means used to collect information, whether it be through satellite imagery, aerial photography, field survey or using a combination of sources.
I. Introduction

## Slide 6
1.3 Classification method introduction through PolSARPro
Pixel based Object based
UnsupervisedSupervised
-Currently only pixel based classifier
-Object based is not available
I. Introduction

## Slide 7
Features available in PolSARPro:
(1) Matrix elements, eg. [T3]
(2) Polarimetric decomposition features
eg. H/A/Alpha decomposition
  1.4 Feature selection and transformation
All the elements can be used as features
I. Introduction

## Slide 8
  1.4 Feature selection and transformation
Features available in PolSARPro:
(2) Polarimetric decomposition features and many others provided by PolSARPro:
But it does not mean the more the better for classification:
Dimension disaster problem:
With fixed training samples, accuracy increases with dim to one maximum acc., then decreases
The key reason is there are correlations between features , and more feature needs more training samples to solve the classification model.
PorSARPro solution:
SVM supervised classification, lets you to choose features.
I. Introduction

## Slide 9
I. Introduction
  1.5 Classifier training and testing
“spectral classes “ and “informative classes”
  Spectral classes
    Classes can be spectrally separated, optical remote sensing
    Classes can be separated by polarmteric mechanism or PolSAR data itself
  Informative classes: useful for real applications
But,
Without training it is harder to get informative classes
RS data
Classifier training
Informative classes
Training samples
Accuracy testing samples
Map output
RS data
Unsupervised classification
Spectral classes
Classes combination
Informative classes
Map output
Supervised classification
Un-supervised classification

## Slide 10
II. GF-3 PolSAR dataset
2.1 The Specifications of GF-3 Satellite
Parameter | Specification
Orbit altitude | 755 km
Orbit type | Sun synchronization repeating orbit
Revisit cycle | 29 days
Band | C
Incidence angle | 10°～60°
High spatial resolution (1 m)
Multi imaging mode (12 types)
Universal application (Ocean, Disaster reduction, Meteorology)
Advantages:

## Slide 11
II. GF-3 PolSAR dataset
2.1 The Specifications of GF-3 Satellite
NO. | Mode | Incidence angle | Resolution (m) | Width (Km) | Polarization
1 | SL | 20-50 | 1 | 10 | Single
2 | UFS | 20-50 | 3 | 30 | Single
3 | FSI | 19-50 | 5 | 50 | Dual
4 | FSII | 19-50 | 10 | 100 | Dual
5 | SS | 17-50 | 25 | 130 | Dual
6 | QPSI | 20-41 | 8 | 30 | Full
7 | QPSII | 20-41 | 25 | 40 | Full
8 | NSC | 17-50 | 50 | 300 | Dual
9 | WSC | 17-50 | 100 | 500 | Dual
10 | GLO | 17-53 | 500 | 130 | Dual
11 | WAV | 20-41 | 10 | 5 | Full
12 | EXT | 10-60 | 25 | 80 | Dual
Spotlight
Stripmap
ScanSAR

## Slide 12
II. GF-3 PolSAR dataset
2.2 Practical Data of GF-3
Azimuth
Range
Test Area
  GF-3 PolSAR Data
Observation Mode:
QPSΙ (Quad Polarization Strip Ι)
Observation Date:
Aug. 03. 2017.
Pixel Spacing(azimuth×range):
5.01 m × 4.50 m.
Center incidence angle:
48.8°
Calibrated and Multi-look ( 2 × 2) processed Result (Pauli RGB)

## Slide 13
II. GF-3 PolSAR dataset
2.3 GF-3 PolSAR PauliRGB and the key landcover types
Subset Test Area
Forest

## Slide 14
II. GF-3 PolSAR dataset
Subset Test Area
Wheat
2.3 GF-3 PolSAR PauliRGB and the key landcover types

## Slide 15
II. GF-3 PolSAR dataset
Subset Test Area
Cole
2.3 GF-3 PolSAR PauliRGB and the key landcover types

## Slide 16
II. GF-3 PolSAR dataset
Subset Test Area
Grass
2.3 GF-3 PolSAR PauliRGB and the key landcover types

## Slide 17
III. Practical
[T3] elements
Decomposition parameters
H/A/alpha classification
H/A/alpha WISHART classification
SVM supervised classification

## Slide 18
PolSARpro - Bio SOFTWARE

## Slide 19
[T3] ELEMENTS
Do it Yourself:
Select some elements, set the parameters and view the corresponding BMP files (select BMP).
DATADIR
T3
config.txt
[T3x3] Elements
Txy_mod.bin
Txy_db.bin
Txy_pha.bin
Txy_mod.bmp
Txy_db.bmp
Txy_pha.bmp

## Slide 20
DECOMPOSITION PARAMETERS
Do it Yourself:
Select some elements, set the parameters (Nwin = 1) and view the corresponding BMP files (select BMP).
1
1

## Slide 21
[T3] ELEMENTS
T11_dB
T22_dB
T33_dB

## Slide 22
[T3] ELEMENTS
span_dB
T12_pha

## Slide 23
PolSARpro - Bio SOFTWARE

## Slide 24
DECOMPOSITION PARAMETERS
Do it Yourself:
Select some elements, set the parameters (Nwin = 3) and view the corresponding BMP files.

## Slide 25
DECOMPOSITION PARAMETERS
Entropy
Lambda

## Slide 26
DECOMPOSITION PARAMETERS
Alpha
Lambda

## Slide 27
DECOMPOSITION PARAMETERS
Anisotropy
Lambda

## Slide 28
DECOMPOSITION PARAMETERS
Anisotropy
Entropy

## Slide 29
DECOMPOSITION PARAMETERS
(1–H) A
(1-H) (1-A)
low entropy and low anisotropy
low to medium entropy

## Slide 30
DECOMPOSITION PARAMETERS
H (1-A)
HA
high entropy and high anisotropy
high entropy and low anisotropy

## Slide 31
PolSARpro - Bio SOFTWARE

## Slide 32
H / A / alpha CLASSIFICATION
Do it Yourself:
Select some elements, set the parameters (Nwin = 3) and view the corresponding BMP files.

## Slide 33
DATADIR
entropy.bin, anisotropy.bin, alpha.bin
combination_HA.bin, combination_1mHA.bin,
combination_H1mA.bin, combination_1mH1mA.bin
H_A_class.bin, H_Alpha_class.bin, A_Alpha_class.bin
config.txt
entropy.bmp, anisotropy.bmp, alpha.bmp
combination_HA.bmp, combination_1mHA.bmp,
combination_H1mA.bmp, combination_1mH1mA.bmp
H_A_class.bmp, H_Alpha_class.bmp, A_Alpha_class.bmp
H_A_occurence.bmp, H_Alpha_ occurence.bmp,
A_Alpha_ occurence.bmp, H_A_segmented.bmp,
H_Alpha_ segmented.bmp, A_Alpha_ segmented.bmp
HAlphaLambda_RGB.bmp, HAAlpha_RGB.bmp
HACombinations_RGB.bmp
[T3x3] Elements
H / A / alpha CLASSIFICATION
Do it Yourself:
Select some elements, set the parameters (Nwin = 1) and view the corresponding BMP files.

## Slide 34
H / A / alpha CLASSIFICATION

## Slide 35
H / alpha / Lambda CLASSIFICATION
Do it Yourself:
Select some elements, set the parameters (Nwin = 1) and view the corresponding BMP files.
1
1

## Slide 36
DATADIR
config.txt
[T3x3] Elements
H_alpha_lambda_class1(2,3).bin,
H_alpha_lambda_occurence_class1(2,3).bin,
H_alpha_lambda_segmented_class1(2,3).bin,
H_alpha_lambda_class.bin,
H_alpha_lambda_class1(2,3).bmp,
H_alpha_lambda_occurence_class1(2,3).bmp,
H_alpha_lambda_segmented_class1(2,3).bmp,
H_alpha_lambda_class.bmp,
Do it Yourself:
Select some elements, set the parameters (Nwin = 3) and view the corresponding BMP files.
H / alpha / Lambda CLASSIFICATION

## Slide 37
Low l
Medium l
High l
H / alpha / Lambda CLASSIFICATION

## Slide 38
Low l
H / alpha / Lambda CLASSIFICATION

## Slide 39
Medium l
H / alpha / Lambda CLASSIFICATION

## Slide 40
High l
H / alpha / Lambda CLASSIFICATION

## Slide 41
H / alpha / Lambda CLASSIFICATION

## Slide 42
PolSARpro - Bio SOFTWARE

## Slide 43
WISHART - H/A/alpha CLASSIFICATION
Do it Yourself:
Set the parameters, run and view the corresponding BMP files.
1
1

## Slide 44
DATADIR
config.txt
Wishart_H_alpha_class_X.bin
Wishart_H_A_alpha_class_X.bin
Wishart_H_alpha_class_X.bmp
Wishart_H_A_alpha_class_X.bmp
X = window size
[T3x3] Elements
Do it Yourself:
Set the parameters, run and view the corresponding BMP files.
WISHART - H/A/alpha CLASSIFICATION

## Slide 45
WISHART - H/A/alpha CLASSIFICATION

## Slide 46
WISHART - H/A/alpha CLASSIFICATION

## Slide 47
We started this practical session from T3 matrix that has been calibrated and multi-look processed.
GF-3 QPSI Quad-Pol
Range pixel spacing:
9.0 m
Azimuth pixel spacing:
10.0 m
GF-3 PolSAR Raw Data
Multi-Look
T3 Matrix
SVM classifier
Classification Result
Features Extraction
Sample Data
Import and Calibration
Speckle Filter
SVM supervised classification

## Slide 48
SVM supervised classification
Step-1: Define classification system & classification legend
Wheat
Cole
Forest
Grass
Legend:
Classification system:
耕地(crop land)
1.1 水田(paddy)
1.2 水浇地(irrigated)
1.2 旱地(dry)
2. 园地(garden)
3. 林地(forest)
3.1 乔木林地(arbor)
3.2 竹林地(bamboo)
…
4. 草地(grass land)
4.1 天然牧草地(natural grass land)
…
5. 商服用地(commercial)
6.
…
12. 其他土地(others)

## Slide 49
Step-2: Speckle Filter

## Slide 50
PauliRGB
After Filter
PauliRGB
Before Filter
1
2
Step-2: Speckle Filter

## Slide 51
Step-3: Features Extraction
entropy.bin
anisotropy.bin
alpha.bin
Polarization features:

## Slide 52
Step-4: SVM classifier
1
2
3
4
Select the training sample data.
Select the classification features
Select the Kernel function
Run Classification

## Slide 53
Step-4: SVM classifier
Select the training sample data.

## Slide 54
Step-4: SVM classifier
Select the training sample data.
Select button
Open the menu
Zoom button
Basic operation:

## Slide 55
Step-4: SVM classifier
Select the training sample data.
Basic operation:
Add a new class 1.
Select first area for class1
  Click ‘Select area’ , draw a polygon
  Click ‘Select area’ , stop drawing;
  Click ‘Delete area’ .
Select second area for class1;
....
Add a new class 2.
Select first area for class2;Select second area for class2;....
....
Save configuration

## Slide 56
Forest
Grass
Wheat
Cole
Step-4: SVM classifier
Select the training sample data.
Do it yourself.
Prepare the training sample data

## Slide 57
Step-4: SVM classifier
2. Select the classification features
Select the features that need to be added to the classifier

## Slide 58
3. Select the Kernel function
We choose polynomial kernel function
Degree:2
4. Run Classification
3
4
Step-4: SVM classifier

## Slide 59
Classification result vs. GF-3 PolSAR Pauli-RGB image
Forest
Grass
Wheat
Cole
Cole
II. GF-3 PolSAR dataset

## Slide 60
Thanks