## Landslide classification with the Cruden-Varnes method

In the following examples the landslide type is classified following Cruden and Varnes (1996).

Photographs are taken from USDC-NGDC Geologic Hazard CD-ROM (Hittelman et al, 1994).

### Example 1:

Talus cones formed from rockfall in Glen Canyon, above Kane Creek (Arizona, USA)

Figure 1-cvc1

Classification: Active, enlarging, successive, extremely rapid dry rock fall

### Example 2:

Rock slide of 1903 at Frank, Alberta (Canada). In less than 2 minutes 40 million cubic yards of rock from Turtle Mountain slid along a plane of structural weakness to cover the town of Frank.

Figure 1-cvc2

Classification: Dormant, complex, extemely rapid, dry rock fall-debris flow

### Example 3:

In 1970, an earthquake-induced rock and snow avalanche on Mt. Huascaran, Peru, buried the towns of Yungay and Ranrachira, with a death toll of 66,700. The avalanche started with a sliding mass of ice and rock about 1 km wide and 1.6 km long that swept downslope about 14.4 km with an average speed of 160 km/h. Moraine material was picked up and by the time it reached Yungay, it had a volume of 2.2 million km3 of water, mud and rocks.

Figure 1-cvc3

Classification: Dormant, complex, extremely rapid, wet, rock slide-debris flow

### Example 4:

Results of the 1963 rockfall avalanche of volcanic debris on Little Tahoma, Mt.Rainier, Washington (USA).

Figure 1-cvc4

Classification: dormant, complex, extremely rapid, wet, rock fall-debris flow

### Example 5:

Earthquake-induced slide downstream side of Madison River, Montana (USA). Light coloured rock is dolomite marble, the more resistent rock that supported weathered mica-rich, overlying layers. An earthquake in 1959 fractured the dolomite and caused a great avalanche of rock, dirt, and trees to cascade from the steep south wall of Madison River Canyon, about 394 m above the canyon floor. The movement formed a barrier that blocked the gorge and created a lake.

Figure 1-cvc5

Classification: dormant, single, extremely rapid, rock slide

### Example 6:

Mudflow scar in Never-Summer range, Rocky Mountain National Park (Colorado, USA), one month after the event in June 1978. The flow consisted of colluvium deposits on bed rock and was triggered by an irrigation ditch that leaked water.

Figure 1-cvc6

Classifcation: dormant, single, extremely rapid, wet debris flow

### Slide 7:

The Slumgullian mudflow in the San Juan Mountains dammed lake Fork, and formed Lake San Cristobal (lower left) at Lake City, Colorado. The flow is still active.

Figure 1-cvc7

Classification: active, moving, slow (?), wet (?) earth flow

### Example 8:

Earthflow in Rapid Bay, Southern Australia.

Figure 1-cvc8

Classification: dormant, single, moderately slow, wet earth flow

### Example 9:

Slump on the Pacific Palisades in Southern California. Two slumps are visible, one at the center just below the road and the other one behind the first.

Figure 1-cvc9

Classification: active, retrogressive, multiple, slow earth slide

### Example 10:

Recently reactivated slump/earthflow below Chalet du Fer Leysin, Switzerland. The material consits of colluvium on bedrock.

Figure 1-cvc10

Classification: reactivated, advancing, succesive, moderately slow, wet earth slide

Example 11:

Rock glaciers in tertiary rock on mt. Sopris, Colorado

Figure 1-cvc11

Classification: relict, succesive, extremely slow, dry, debris flow (?????)

Back to Landslide Classification Systems