## Examples of input maps: landslide inventory maps

Landslide inventory maps show the location, typology, activity and component (scarp area, transportation zone, or accumulation zone) of landslides for different periods. Such maps provide detailed information on the landslides that have occurred in the area, and therefore form the starting point for many types of analysis that are based on the principle “the past is the key to the future”. Landslide inventory maps are made through a combination of image interpretation and fieldchecking. They can be accompanied by a landslide database, in which all landslides that have happened in an areas are systematically recorded.

Current landslide inventory maps are not standardized around the world. They are published at different scales with various levels of details. These maps usually include information on the classification of the landslide type, their location, as well as the geomorphic and slope characteristics. In some cases, active and dormant landslides are distinguished. In other cases, the information is included on geological and soil degradation maps.

Figure 3-example5 shows

Figure 3-example5